## Slide 1: Experience with the recent release of MELCOR at UJV Rez for VVER-1000 analyses with focus on iodine forms in the containment
Miroslav Kotouč

## Slide 2: Outline
More realistic iodine representation in MELCOR simulations
  CsI vs. I2
Disappearance of UO2/decay heat from the simulation
  For the VVER-440
Testing the r2023.0.9 vs. r2024.0.0 on identical VVER-1000 input deck
  CTMT long-term pressurization

## Slide 3: iodine representation in melcor

## Slide 4: forms of iodine in melcor
Goal: estimate properly/realistically ST onto the FCVS filters
MELCOR default: class combination ‘CS’ + ½*’I2’ => ‘CSI’
=> practically all ‘I2’ class transfers into the ‘CSI’ class, which might bias the results taking into account that:
    CsI (~aerosols) gravitationally settle
      MELCOR does not allow for mechanistic resuspension of RNs from water sumps
    Filters are more efficient for aerosol (DF~104) than for gaseous iodine (DF~102)
    Correct speciation is important also for radiological consequences assessment
NUREG-1465 estimated the approximate amount of CsI => CTMT:
I.e., up to ~5 % of iodine shall be treated as gaseous iodine in the CTMT
Moreover, iodine in the CTMT undergoes chemical-physical reactions
DFM-type of filter unit proposed for the Temelin NPP (VVER-1000)
Detailed FCVS duct model
Integral CTMT model
MELCOR UG (2024)

## Slide 5: finding realistic iodine speciation
Study performed in 3 steps:
  MELCOR integral analysis => sources of m/H/RN
    Assuming 5 % of iodine in the ‘I2‘ class and 95 % of I in the ‘CSI’ class
  COCOSYS CTMT analysis <= sources of m/H/RN
    advanced chemical reactions, pH in the sumps, dose rate and wet/dry painted/steel/concrete surfaces
  MELCOR integral analysis with the COCOSYS-calculated long-term ‘I2‘ class mass
Integral MELCOR simulation
…
…
…
Detailed COCOSYS CTMT response
Specific decay power history
Initial mass: ’I2’+2*’CS’
Must be new element
Absolute values
Cs M [kg/kmol] | 132.91
I M [kg/kmol] | 126.9
I i. i. [kg] | ~20

## Slide 6: SPECIATION of iodine: cocosys analysis
MELCOR integral analysis (fixed 5 % of I2)
sources into EDF
COCOSYS CTMT analysis
stand-alone calc. based on MELCOR sources
pH=5; P=2 kGy/hr

## Slide 7: cocosys ctmt results
Iodine dissolved in sumps
Airborne aerosols
Molecular (I2) ~0.31 kg
Organic
Initial inventory of iodine ~20 kg => 0.31 kg of I2 makes ~1.56 % of iodine in the ‘I2‘ class!
M. Leskovar, “Uncertainty Analysis of Severe Accident Scenario in Krško NPP,” Proceedings of the International Conference Nuclear Energy for New Europe, Portorož, Slovenia, September 11-14 (2023).

## Slide 8: sensitivity study: iodine representation
MELCOR integral calculation: Guillotine-Break LOCA
FCVS in operation after reaching 0.58 MPa(abs)
3 cases for iodine representation:
  „CsI“ (red curves in the graphs)
    automatic CsI formation is allowed
    automatic Cs2MoO4 formation is allowed
  „1.56I2“ (green curves in the graphs)
    1.56 % of iodine => ‘I2’ class
    98.44 % of iodine => ‘CSI’ class
    automatic Cs2MoO4 formation is allowed
  „3.00I2“ (blue curves in the graphs)
    3.00 % of iodine => ‘I2’ class
    97.00 % of iodine => ‘CSI’ class
    automatic Cs2MoO4 formation is allowed

## Slide 9: g-loca scenario: decay heat
CsI
1.56I2
3.00I2
Instants of RPV failure
Not monotonic behavior observed
FPs release

## Slide 10: g-loca scenario: rpv water level
CsI
1.56I2
3.00I2
Instants of RPV failure
Again, no pattern found for the in-vesel phase & amount of CsI; some similarity for the fixed ‘I2’ amount

## Slide 11: g-loca scenario: pd/mp in lower p.
CsI
1.56I2
3.00I2
Instants of RPV failure
Again, cases with the fixed ‘I2’ amount are similar

## Slide 12: g-loca scenario: ctmt pressure
CsI
1.56I2
3.00I2
Instants of FCVS opening
Rather big discrepancies in CTMT failure times; related to I2 (volatile) content in the atmosphere?

## Slide 13: g-loca scenario: ‘i2‘ release
CsI
1.56I2
3.00I2
Instants of FCVS opening
Releases of ‘I2’ onto the FCVS filters is proportional to the fixed amount of ‘I2’
Whole ‘I2’ class is located in the CTMT, almost solely as airborne
Some adsorption…

## Slide 14: g-loca scenario: ‘csi‘ release
CsI
1.56I2
3.00I2
Instants of FCVS opening
‘CSI’ (aerosols) willingly settle
Expected: a little less ‘CSI’ for the 3 % of ‘I2’ than for the 1.56 % of ‘I2’
Much less ‘CSI’ mass released: this means MELCOR correctly combines ‘CS’ and ‘I2’ with the factor of 0.5 for ‘I2’

## Slide 15: g-loca scenario: ‘cs‘ release
CsI
1.56I2
3.00I2
Instants of FCVS opening
Less ‘CSI’ is created => more ‘CS’ remains and is released
Expected: more ‘CS’ release for the 3 % of ‘I2’ and thus less amount of ‘CSI’, thus more available ‘CS’
‘CS’ (aerosols/vapors) willingly settle/condense

## Slide 16: disappearance of uo2/decay heat

## Slide 17: vver-1000 input deck: decay heat
Instant of RPV failure
RN total decay heat starts to deviate
DCH total decay heat according to the table

## Slide 18: vver-1000 input deck: uo2 mass
Instant of RPV failure

## Slide 19: vver-440 input deck: decay heat
RN1-DHTOT starts to diminish before RPV failure!!!
RN1-DHCOR according to the FPs release
DCH-TOTCLSPOW as expected

## Slide 20: vver-440 input deck: uo2 mass
Why is the total amount of UO2 decreasing?!?!

## Slide 21: vver-440 input deck: MEGouT(melOUT) errors
MEGOUT: no error…
MELOUT: same masses, but error 34 tons!?!?...

## Slide 22: r2023.0.9 vs. r2024.0.0

## Slide 23: identical vver-1000 input: ctmt pressure
r2024.0.0
r2023.0.9
HS package: 2D HSs not active yet…?

## Slide 24: A few conclusions/observations
It is important to estimate before-hand the form of iodine expected to exist in long-term in the CTMT:
  Gaseous I2 naturally increases the ST into the environment/FCVS filters
  The proposed fixed amount of ‘I2’ class is ~1.56 acording to COCOSYS
  The right way of combining ‘CS’ with ‘I2’ is to use the molar ratio
    2 … for automatic ‘CSI’ creation
    1 … for manual setting the‘CSI’ mass
For the VVER-440 input deck, we do lose UO2 mass and decay heat from the simulation right after the onset of fuel degradation
Unexpected large differences in CTMT pressure when testing the r2024 MELCOR release

## Slide 25: Thank you for your attention!
ÚJV Řež, a. s. Hlavní 130, Řež 250 68 Husinec, Czech Republic e-mail: sales@ujv.cz
www.ujv.cz

## Slide 26: g-loca scenario: decay heat in RN classes
Chart: Decay power per RN classes
Total (whole-core) decay heat
Halogens RN class decay heat
0.00, 1.56 or 3.00 % of iodine as ‘I2’, i.e. in the atmosphere, is rather marginal…